## Slide 1: Hyperspectral Rendering in Radiance
Greg Ward, Anyhere Software

## Slide 2: Talk Outline
Introduction and context
New Radiance primitives
New rendering parameters
Radiance tools for hyperspectral
Example scene with comparisons
Discussion and future outlook
Conclusion

## Slide 3: What Is Radiance?
“Radiance” is a software package first developed in the late 1980’s and still in use by building researchers and designers today
Radiance is a unit of light flux measurement (watts/steradian-meter2 in SI units)
Spectral radiance subdivides light over multiple wavelengths

## Slide 4: Radiance Rendering

## Slide 5: Corresponding Luminance

## Slide 6: What Is Hyperspectral?
Traditional rendering uses RGB to represent color values
  3x3 matrix to CIE XYZ colorimetry
Hyperspectral rendering divides spectrum into >3 (typically ≥9) bands
Spectral limits may exceed those of human visual response (IR, UV)
More accurate with new applications

## Slide 7: Current Impetus
Many researchers and practitioners are concerned with melanopic response
  melanopic ≠ photometric sensitivity
  distrust of approximations from RGB
Active research in terrestrial solar and sky spectra
Current methods mostly retrace rays using Radiance

## Slide 8: Advantages of Native Hyperspectral Rendering
More efficient, since rays do not need to be stored or retraced
Retracing rays also leads to chromatic noise due to non-repeating ray trees
New HSR (hyperspectral radiance) image format introduced
  new tools for HSR display and calcs

## Slide 9: Sensitivity Curves
Melanopic
Scotopic
Photopic

## Slide 10: Radiance System Design
Scene format has 3-component colors baked into material primitive types
Initially contemplated redesign of scene description based on “Materials and Geometry Format” (MGF)
  would have required full rewrite of existing rendering code
  MGF colors covers visible spectrum only

## Slide 11: Hyperspectral Extensions
While Radiance material types only support 3 spectral samples, new pattern primitives are multi-spectral:
  “spectrum” is a basic spectral color
  “specfile” takes static spectrum from file
  “specfunc” is dynamic and procedural
  “specdata” is dynamic and data-driven
  “specpict” maps a hyperspectral image

## Slide 12: How Spectral Patterns Work
Depending on the primitive it modifies, a spectral pattern typically multiplies a material’s RGB color to determine reflectance or transmittance
Multiplication rules are based on “partition” wavelengths that define RGB bands

## Slide 13: Partitioning the Spectrum
Spectrum is partitioned into wavelengths of 380-480nm for BLUE, 480-588nm for GREEN, and 588-780nm for RED for purposes of multiplication between material colors and spectral patterns
Extrema may be adjusted to cover UV and/or IR if desired, which does not alter the range of GREEN, only BLUE and RED
The number of spectral samples may be set from 3 to MAXCSAMP (24 in 6.0a prerelease)

## Slide 14: Example Spectrum
void spectrum gold_spec
0
0
82 380 775 0.389133964 0.389133964 0.389255302 0.389980986 0.391051245
0.392138273 0.392908482 0.393032534 0.392429968 0.391351324
0.390030615 0.388650157 0.387407915 0.386320218 0.385530031
0.385510124 0.386040307 0.386026057 0.388298949 0.394215681
0.404140535 0.419966115 0.443246002 0.473861019 0.511014174
0.552643396 0.596304788 0.639685049 0.682955923 0.723645597
0.759200442 0.789126545 0.813469177 0.832955943 0.848265499
0.860485356 0.870549939 0.878925721 0.885276016 0.891159039
0.896546999 0.901393946 0.905636686 0.909327028 0.912475235
0.91521538 0.917680109 0.919998384 0.922297675 0.924966158
0.927728576 0.930571538 0.933477024 0.936421086 0.939377245
0.942439249 0.945588396 0.948563802 0.951319598 0.953828111
0.956075841 0.958059262 0.959789105 0.961306963 0.96261608
0.963753124 0.964748535 0.965627808 0.966413149 0.96712339
0.967778124 0.968398351 0.968976934 0.969517604 0.970024269
0.970500409 0.970949021 0.971372989 0.971775043 0.972157635
gold_spec metal gold_smat
0
0
5 1 1 1 1 0
Starting λ
Ending λ
Multiplies spectrum
Notes: Spectral patterns accept whatever sampling you provide, then (usually) resample to fit active rendering parameters.

## Slide 15: New Rendering Parameters
Supported by all renderers (rpict, rvu, rtrace, & rcontrib):
-cs N # number of spectral samples (default is 3)
-cw w1 w2 # spectrum equally divided from w1 to w2 (nm)
Supported by rpict and rtrace:
-pRGB # output RGB color space (default)
-pXYZ # output XYZ color space
-pc xr yr xg yg xb yb xw yw # output custom color space
Supported by rtrace only:
-pY # output single-channel photopic luminance
-pS # output single-channel scotopic luminance
-pM # output single-channel melanopic luminance
-co+ # output N-channel spectral color (also rtpict)
Note: rcontrib always produces full spectral output based on -cs
Notes: Default wavelength limits are 380 - 780 nm.

## Slide 16: New HSR Image Format
HSR for “Hyperspectral Radiance” uses similar common-exponent encoding to RGBE and XYZE (i.e., HDR format)
Can be produced by rtrace, rcontrib, or rtpict
Can be used by “specpict” primitive
Can be manipulated by pfilt, rcode2bmp, rcomb, rcrop, and rmtxop tools

## Slide 17: Example with rtpict & rcomb
Render a hyperspectral image with rtpict and anti-alias with pfilt:
rtpict -vf myview.vf -x 2048 -y 2048 -cs 18 -co+ specscene.oct \
| pfilt -1 -x /2 -y /2 -r .6 > specim.hsr
Convert result to RGB image and melanpopic pixel array using rcomb:
rcomb specim.hsr -c RGB -fc > rgbim.hdr
rcomb specim.hsr -c M -ff > melim.mtx
Tone-map result into 24-bit BMP image:
rcode2bmp specim.hsr
(open “specim.bmp”)

## Slide 18: New rcomb Tool
rcomb sits halfway between rmtxop, which performs matrix operations, and pcomb, which combines HDR images
Less memory for supported operations
  i.e., everything but transpose operation or concatenating more than two matrices
  can stream inputs with ∞ rows
Programmable like pcomb, but for matrix and HSR input and output

## Slide 19: Example Spectral Scene
BlueFlower
Red
Blue
Gold
Neutral.8
Fluorescent
MacBeth Colors

## Slide 20: MacBeth Reflectance Spectra

## Slide 21: Fluorescent Lamp Spectrum

## Slide 22: Error from Rendering in RGB

## Slide 23: RGB Rendering

## Slide 24: Reference Solution (81 spectral samples)

## Slide 25: Rendering with 6 Spectral Samples

## Slide 26: Error with 6 Spectral Samples
Notes: Worse due to advantage of rendering in color space related to eye’s effective response

## Slide 27: 9 Spectral Sample Error

## Slide 28: 12 Spectral Sample Error

## Slide 29: 15 Spectral Sample Error

## Slide 30: 18 Spectral Sample Error

## Slide 31: 21 Spectral Sample Error

## Slide 32: 24 Spectral Sample Error

## Slide 33
Rendering Time for Different Spectral Sample Densities

## Slide 34: Photopic Luminance

## Slide 35: Melanopic Luminance (from 24 spectral samples)

## Slide 36: Melanopic Luminance (estimated from RGB)

## Slide 37: Relative Error from Using RGB Estimate
-25%
+25%
0

## Slide 38: Points for Discussion
Improvement levels off around 18 samples, at least for this scene
Benefits of RGB color space over straight spectral rendering means we don’t see advantage until 9 samples
Better selection of RGB primaries leads to more accurate results (EGWR ‘02)
Extending beyond visible limits?

## Slide 39: Error from Rendering in RGB

## Slide 40: Using Sharpened RGB Space

## Slide 41: Extending Spectral Bounds
380-780 nm is used for most situations
Extending to NIR works OK, but far infrared of ~3000-100000 nm is issue for uniform wavelength steps
Uniform steps in frequency would make more sense, but conflicts with current measurement conventions

## Slide 42: Future Work (1)
Further testing is needed (from you)
  6.0a installers available from GitHub
Photon-mapping is currently broken with spectral rendering turned on
  waiting on Roland Schregle to update it
May add HSR output to rpict at some point, but this faces challenges
  image plane sampling is main problem

## Slide 43: Future Work (2)
Holly Rushmeier has NSF grant to look at sharing information, code for hyperspectral rendering
Taoning Wang and other researchers are working on spectral sky models
Need to make changes/additions to annual simulation methods for multi-spectral (gendaylit, gendaymtx, etc.)

## Slide 44: Conclusions
New spectral sampling can improve accuracy for some situations
  includes support for melanopic response
Much work remains on the data side
  sky models and measurements
  materials, possibly BSDFs
Incorporating code into 3rd party tools and interfaces